## Slide 1: LIQUEFACTION-INDUCED SETTLEMENT OF SHALLOW FOUNDATIONS AND REMEDIATION: 3D NUMERICAL SIMULATION
By AHMED ELGAMAL , JINCHI LU & ZHAOHUI YANG

## Slide 2: Response characteristics and Discussion
Site response (Case MSID)
Figures 5 and 6 display lateral acceleration and excess pore pressure (u,) time
histories at different depths for Case MSlD. Figure 6 shows that the entire sand
stratum was liquefied throughout (maximum excess pore-pressure u, equals the
initial overburden vertical effective stresses oLo, i.e. the porepressure ratio Tu =
ue/u~=, '1.0). Initial liquefaction was reached at 9 seconds bear the surface (Fig. 6),
propagating downwards throughout the stratum after about 13 seconds of excitation
(Fig. 6). As liquefaction occurred, acceleration at relatively high levels of input
excitation (during 10-20 s) was clearly attenuated (Fig. 5).
Once liquefaction was reached, r, remained at 1.0 with reduction only taking
place near the end of shaking, from the base upwards. The stress-paths and stressstrain
history of Fig. 7 show the typical mechanism of cyclic decrease in effective
confinement due to pore-pressure buildup, along with the associated loss in shear
stiffness and strength.

## Slide 3
Benchmark simulation (Case MS)
In the free field (not shown), the response was essentially the same is that of
MS1D. Under the foundation, strong dilative response was observed. As shown in
Fig. 8, a number of instantaneous sharp pore pressure drops occurred. This dilative
response is also observed in the stress paths as shown in Fig. 9. In the soil section
immediately below the foundation, u. buildup was relatively slow (top graph of
Fig. 8). This pattern of response was caused mainly by the shear-induced dilative
response during the deformation of the saturated soil below the foundation [Liu
and Dobry, 1997; Adalier et at., 19983. As the rate of settlement decreased (MS in
Fig. 4), u, under the foundation (top graph of Fig. 8) built up rapidly and only
started to dissipate after nearly reaching liquefaction at about 110 seconds (well
after the end of shaking at 98 seconds). The permanent foundation settlement was
0.23 rn (Table 1) in Case MS. Similar characteristics of u, response were recorded
during the centrifuge test of Liu and Dobry (corner of Fig. 8).

## Slide 4
Compaction remediation
Cases DS, DSL and DSL4 were compacted to different lateral extent and soil depth
levels (Table 1 and Fig. 1). The response recorded away from the foundation (fieefield)
in all these cases was quite similar to that of Case MS (not shown). Under
the foundation, the response (e.g. lateral acceleration and excess pore pressure time
histories) in cases DS, DSL and DSL4 were also quite comparable to Case MS.
Pore-pressure for DSL4 under the foundation is shown in Fig. 10. Note the
similarity to MS (Fig. 8), with u, rising near the end of shaking (even at 4m and
6 m depth in DSLQ), and the somewhat faster dissipation of u, at 8m depth.