## Slide 1: Opensees code for plane strain, single element, dynamic analysis (input motion: sinusoidal acceleration at base)
By
Jubin kumar soni

## Slide 2: Following steps to be followed when dynamic analysis to be done in geotechnical problem
1.defining physical properties of element
2.creating model builder
3.define material and properties
4.define the nodes
5.define elements
6.fix the base of element
7.set time equal to zero
8. create a LoadPattern
9.create the Analysis
10. create the recorder
11.analyze
12print result

## Slide 3: 1.Defining physical properties of element
set accMul 9.81 ;
set massDen 2.000 ;# solid mass density
set fluidDen 1.0 ;# fluid mass density
set massProportionalDamping 0.0 ;
set stiffnessProportionalDamping 0.001 ;
set cohesion 30 ;
set peakShearStrain 0.1 ;
set E1 90000.0 ;#Young's modulus
set poisson1 0.40 ;
set G [expr $E1/(2*(1+$poisson1))] ;
set B [expr $E1/(3*(1-2*$poisson1))] ;
set press 0 ;# isotropic consolidation pressure on quad element(s)
set period 1 ;# Period of applied sinusoidal load
set deltaT 0.01 ;# time step for analysis
set numSteps 2000 ;# Number of analysis steps
set gamma 0.5 ;# Newmark integration parameter
set pi 3.1415926535 ;
set inclination 0 ;
set unitWeightX [expr ($massDen-$fluidDen)*9.81*sin($inclination/180.0*$pi)] ;# buoyant unit weight in X direction
set unitWeightY [expr -($massDen-$fluidDen)*9.81*cos($inclination/180.0*$pi)] ;# buoyant unit weight in Y direction

## Slide 4: 2.Creating model builder
model basic -ndm 2 -ndf 2

## Slide 5: 3. define material and properties
nDMaterial PressureIndependMultiYield 2 2 $massDen $G $B $cohesion $peakShearStrain
nDMaterial FluidSolidPorous 1 2 2 2.2e6

## Slide 6: 4.Define the nodes
node 1 0.0 0.0
node 2 1.0 0.0
node 3 1.0 1.0
node 4 0.0 1.0

## Slide 7: 5.Define the element
element quad 1 1 2 3 4 1.0 "PlaneStrain" 2 $press 0.0 $unitWeightX $unitWeightY

## Slide 8: 6.Fix the base
fix 1 1 1
fix 2 1 1

## Slide 9: 7.set time equal to zero
setTime 0.0

## Slide 10: 8.create a Load Pattern
pattern UniformExcitation 1 1 -accel "Sine 0 10 $period -factor $accMul"

## Slide 11: 9.create the Analysis
constraints Penalty 1.0e18 1.0e18 ;# Transformation; #
test NormDispIncr 1.e-12 25 0
algorithm Newton
numberer RCM
system ProfileSPD
rayleigh $massProportionalDamping 0.0 $stiffnessProportionalDamping 0.
integrator Newmark $gamma [expr pow($gamma+0.5, 2)/4]
analysis VariableTransient

## Slide 12: 10.Create recorder
recorder Node -file disp.out -time -node 1 2 3 4 -dof 1 2 -dT 0.01 disp
recorder Node -file acce.out -time -node 1 2 3 4 -dof 1 2 -dT 0.01 accel
recorder Element -ele 1 -time -file stress1.out -dT 0.01 material 1 stress
recorder Element -ele 1 -time -file strain1.out -dT 0.01 material 1 strain
recorder Element -ele 1 -time -file stress3.out -dT 0.01 material 3 stress
recorder Element -ele 1 -time -file strain3.out -dT 0.01 material 3 strain

## Slide 13: 11.Analyze commands
set startT [clock seconds]
analyze $numSteps $deltaT [expr $deltaT/100] $deltaT 10
set endT [clock seconds]
puts "Execution time: [expr $endT-$startT] seconds."

## Slide 14: 12.Print result
print node 1
print node 2