## Slide 1: 2D Total Stress Site Response Analysis of a Layered Soil Column
By jubin kumar soni

## Slide 2: Model Description
In this article, the site response analysis are performed for soil deposits which are underlain by an elastic half-space, which simulates the finite rigidity an underlying medium such as bedrock.
It is assumed that there is no groundwater, therefore, total stress analysis is used in this example.

## Slide 3
The soil is modeled in two-dimensions with two degrees-of-freedom using the plane strain formulation of the quad element element.
We considered a soil profile which has a parabolically-increasing shear wave velocity profile with depth and this is accomplished using sublayers

## Slide 4
Schematic representation of the site response model. Node numbers in blue, element numbers in red.

## Slide 5
The horizontal direction is the first degree-of-freedom and the vertical is the second.
The soil node, element, and layer numbering schemes all begin at the bottom

## Slide 6
To account for the finite rigidity of the underlying half-space, a dashpot is incorporated at the base of the soil column using a zeroLength element and the viscous uniaxial material.
Dashpot is assigned a dashpot coefficient equal to the product of the mass density and shear wave velocity of the underlying layer with the area of the base of the soil column.

## Slide 7
The properties of a bedrock layer are used for the half-space. The soil column is excited at the base by a horizontal force time history which is proportional to the known velocity time history of the ground motion.
The horizontal force time history is applied as a Path TimeSeries object using the file, velocityHistory.out.
The force history is obtained by multiplying the known velocity time history by a constant factor set as the product of the area of the base of the soil column (width x thickness) with the mass density and shear wave velocity of the underlying layer.

## Slide 8: Soil Profile Geometry
The soil profile geometry is controlled entirely by the thickness of the soil deposit. In this example, this value is set at 40 meters.

## Slide 9: Mesh Geometry
The geometry of the mesh is based upon the concept of resolving the propagation of the shear waves below a particular frequency by ensuring that an adequate number of elements fit within the wavelength of the chosen shear wave.
This ensures that the mesh is refined enough such that the desired aspects of the propagating waves are well captured in the analysis.

## Slide 10
This is accomplished in the model by specifying the highest frequency which the user wishes to be well resolved and the number of elements that the user desires to be in one wavelength of a shear wave propagating at this frequency.
The wavelength used to define the mesh geometry is determined by dividing the minimum shear wave velocity of the soil profile by the specified cutoff frequency.
In the provided examples there are either 8 or 10 elements per wavelength.
The largest value possible value for the specified frequency is the sampling frequency of the ground motion. The provided examples use 100 Hz for the cutoff frequency.

## Slide 11
The horizontal size of the elements is set to be the minimum vertical element size in the soil column. The number of nodes and the total number of elements are computed automatically. The number of elements is based on the computed element size and the thickness of the soil deposit. For n total elements, there are 2n + 1 total nodes.

## Slide 12: Soil Nodes
The soil nodes are created automatically from the input geometry and meshing information.
The node numbering scheme is left-to-right, top-to-bottom.
Nodes with even numbers fall on the y-axis, and the odd-numbered nodes are spaced horizontally by the computed horizontal element size.

## Slide 13: Dashpot Nodes
A single zeroLength element is used to define the dashpot, therefore, only two nodes are required.
These nodes are arbitrarily assigned numbers 2000 and 2001.
If there are more than 2000 nodes in the soil column, the dashpot node numbers will need to be changed.

## Slide 14: Boundary Conditions and Equal Degrees-of-Freedom
The nodes at the base of the column are fixed against displacements in the y-direction .The remaining soil nodes are then tied together using the equalDOF command in order to achieve a simple shear deformation pattern. This is done by declaring equalDOF for every pair of nodes which share the same y-coordinate.

## Slide 15
One of the dashpot nodes is fully fixed (node 2000), while the other is fixed only against displacements in the y-direction (node 2001). To incorporate the dashpot element into the total model, equalDOF is again used, this time linking the horizontal degrees-of-freedom of the partially fixed dashpot node and one of the nodes at the base of the soil column.

## Slide 16: Soil Material Properties and Objects
A series of material properties are required to define the constitutive behavior of the soil and the underlying elastic half-space. The main soil properties are the mass density, the shear wave velocity, and Poisson's ratio. From these, the elastic, shear, and bulk moduli are computed. Poisson's ratio is set as zero in these examples for the purposes of emulating a one-dimensional analysis. With Poisson's ratio at zero, no vertical accelerations are generated.
For the case of multiple layers, one material object is created for each layer using the material properties defined in the input file. With the exception of a few global properties, each layer is given a separate set of properties.

## Slide 17: Soil Elements
Four-node quad elements are used to model the soil using the plane strain formulation of the quad element.
The element connectivity uses a counterclockwise pattern for the previously-described node numbering scheme.
The soil elements in each layer are assigned the material tag of the material object corresponding to that layer.

## Slide 18
A unit thickness is used in all examples.
The self-weight of the soil is considered as a body force acting on each element.
The body force is set as the unit weight of the soil in each layer, which is determined from the respective mass density input value.

## Slide 19: Dashpot Material and Element
The viscous uniaxial material is used for dashpot. This material model requires a single input, the dashpot coefficient, c.
Following the method of Joyner and Chen the dashpot coefficient is defined as the product of the mass density and shear wave velocity of the underlying medium, which, in this example, is assumed to have the properties of bedrock.
The dashpot coefficient must also include the area of the base of the soil column to maintain proportional results for any horizontal element size. Since the elements are created with unit thickness, this area is simply the computed horizontal element size.

## Slide 20
A zeroLength element is used for the dashpot. This element connects the two previously-defined dashpot nodes and is assigned the material tag of the Viscous uniaxial material object in the first degree-of-freedom (horizontal direction)

## Slide 21: Recorders
The nodal displacements, velocities, and accelerations in both degrees-of-freedom
The stress and strain response at each point in each element
The recorded nodal values are the true values for each parameter, not relative values as with the uniformExcitation command.

## Slide 22
Two sets of recorders are included to capture the response of the soil during the gravity analysis (which is sometimes useful to ensure proper model generation) and the response of the soil during the application of the ground motion. These files are differentiated by a naming scheme in which the records corresponding to the gravity analysis are named 'Gacceleration', 'Gstress', etc ...

## Slide 23: Gravity Loading and Analysis
The gravity analysis in this example is conducted as a transient analysis with very large time steps
The self-weight of the soil elements provides the loads, therefore, no loading object is required.
Gravity is applied for ten steps with entirely elastic constitutive behavior. This allows the material objects to update various parameters to account for confining pressure.

## Slide 24
Once these steps have converged, the material objects are updated using the updateMaterialStage command to consider elastoplastic behavior, and the gravity analysis is repeated for 40 steps.

## Slide 25: Horizontal Loading and Analysis
Dynamic excitation is applied as a force time history to the base of the soil column, at the node which shares equal degrees-of-freedom with the dashpot.
This force history is obtained by multiplying the velocity time history of the recorded ground motion by the mass density and shear wave velocity of the underlying bedrock layer and the area of the base of the soil column (the horizontal element size in these examples).
This technique considers the finite rigidity of the underlying layer by allowing energy to be radiated back into the underlying material.

## Slide 26
The force history is applied to the model as a Path TimeSeries object using a Plain load pattern object. The actual force applied to the node in each time step is the product of the load factor indicated in the pattern object (1.0 in this), the additional load factor included in the timeSeries object, and the value found in the file, velocityHistory.out, at that time step. The load factor included in the timeSeries object is used to create a force history from the velocity history found in the namesake file.
The transient analysis is conducted with the Newmark integrator using the gamma and beta coefficients defined near the top of the input file. These values are set at 0.5 and 0.25, respectively to ensure there is no numerical damping in the analysis.

## Slide 27
Since these models consider elastoplastic soil behavior, there is inherent hysteretic damping which occurs, however, a small amount of Rayleigh damping is used so there is still some damping at low strain values.
The time step used in the analysis is selected to meet stability considerations using the Courant-Friedrich-Lewy (CFL) condition. Meeting the requirements of this condition ensures that the time step is small enough for stability given the maximum shear wave velocity and the minimum vertical element size in the model.
The example files are set up such that the analysis time step and the corresponding number of steps are automatically generated to satisfy this condition.
If the user alters the shear wave velocity profile such that the lowest layer does not have the highest shear wave velocity, then the value of $vsMax used in this routine will need to be updated.